function [amp, f, ph] = fourierseries(data, Fs, window)
%FOURIERSERIES Fourier series of a time series.
%
% [fft_amplitude, f, fft_phase] = FOURIERSERIES(data, Fs, window)

% Copyright (C) 2014 CNPEM
% Licensed under GNU Lesser General Public License v3.0 (LGPL)

if any(size(data) == 1)
    data = data(:);
end

data = data(:)
Faz a transposta de data

Exemplo:

>> y
y =

     1 2 3

>> y=y(:)
y =

     1
     2
     3

npts = size(data,1);

size(A) returns a row vector whose elements contain the length of the corresponding dimension of A. For example, if A is a 3-by-4 matrix, then size(A)returns the vector [3 4]. The length of sz is ndims(A).
ou seja,
size(A) = (Número de linhas, Número de Colunas)

size(A,dim) returns the length of dimension dim
ou seja,
Retorna o número de linhas para a matriz de dimensão especificada (ou seja, retorna o número de linhas que tem na matriz).

if nargin < 2 || isempty(Fs)
    Fs = 1;
end
nargin returns the number of input arguments passed in the call to the currently executing function. Use this nargin syntax only in the body of a function.
nargin(fx) returns the number of input arguments that appear in the definition statement for function fx.

if nargin < 3 || isempty(window)
    window = rectwin(npts);
end

w = rectwin(L) returns a rectangular window of length L in the column vector w. This function is provided for completeness; a rectangular window is equivalent to no window at all.

window = window(:);

data = data.*repmat(window, 1, size(data,2));

repmat(A,r1,...,rN) specifies a list of scalars, r1,..,rN, that describes how copies of A are arranged in each dimension. When A has N dimensions, the size of B is size(A).*[r1...rN]. For example, repmat([1 2; 3 4],2,3) returns a 4-by-6 matrix.

No nosso caso,
> window é uma matriz de 1 do tipo [Número_pontos_FFT linhas,1]
> size(data,2) retorna o valor 1, pois não temos matrizes com mais de 1 dimensão

o r1 replicaria o conjunto de dados de A r1 vezes linhas, ja o r2 faria semelhante para o número de colunas, conforme exemplo abaixo:

A = diag([100 200 300])
A =

   100 0 0
     0 200 0
     0 0 300

B = repmat(A,2)
B =

   100 0 0 100 0 0
     0 200 0 0 200 0
     0 0 300 0 0 300
   100 0 0 100 0 0
     0 200 0 0 200 0
     0 0 300 0 0 300

A = diag([100 200 300])
A =

   100 0 0
     0 200 0
     0 0 300

B = repmat(A,2,3)
B =

   100 0 0 100 0 0 100 0 0
     0 200 0 0 200 0 0 200 0
     0 0 300 0 0 300 0 0 300
   100 0 0 100 0 0 100 0 0
     0 200 0 0 200 0 0 200 0
     0 0 300 0 0 300 0 0 300

No nosso caso, como r1=r2=1, não faz mudança nenhuma na matriz

amp = abs(fft(data))/npts;
ph = angle(fft(data));

half_npts = ceil((npts+1)/2);

Y = ceil(X) rounds each element of X to the nearest integer greater than or equal to that element.

No caso, ao fazer ceil((npts+1)/2)) serve para garantir que não vamos obter um valor de half_points que não seja inteiro.

amp = amp(1:half_npts, :);
ph = ph(1:half_npts, :);

if rem(npts,2) > 0
    amp = [amp(1,:); 2*amp(2:end,:)];
else
    amp = [amp(1,:); 2*amp(2:end-1,:); amp(end,:)];
end

df = Fs/npts;

f = 0:df:(half_npts-1)*df;